ARWEI-Premium-Reinstreifer

Data Sheet Portal CB 22

Tender Specification:

High quality, especially wear-resistant entrance mat, improved absorption of coarse dirt

Application: Indoor and roofed exterior; normal up to extremely strong frequency, suitable for wheelchairs, overall laying, resting distributed burden up to 1,600 kg per 80 sq. cm

Stripe supporting profile: aluminium, V-shaped; 3 mm ground clearance, uncoupled, sound-absorbing, rinsing, rear ventilated

Cassette brush: with bristle bundles arranged parallel to one another for an improved absorption of coarse dirt, colour black, slip resistance R 12 according to DIN 51130

Connection: ARWEI Special Connectors (patented in 1977); therefore easily to roll up, modular construction – no wire or cable connections -, each part can easily be replaced on the spot

Height: 22 mm

Bar distance 3 mm: Coarse dirt absorption 7.7 l / sq. m

Bar distance 5 mm: Coarse dirt absorption 8.6 l / sq. m

Angle frames in 25 x 25 x 3 mm are available in aluminium or stainless steel.

Changes in construction or due to material reserved in the course of product maintenance. All specifications are standard dimension without consideration of tolerances contingent upon production.

# Text boxes

Cassette brush

ARWEI Special Connectors

Aluminium Profile