ARWEI-Premium-Reinstreifer

Data Sheet Portal GB 23 Mix 2/1

Tender Specification:

High quality, especially wear-resistant entrance mat, improved absorption of coarse dirt

Application: Indoor and exterior; normal up to extremely strong frequency, suitable for wheelchairs, overall laying, resting distributed burden up to 1,400 kg per 80 sq. cm

Stripe supporting profile: aluminium, V-shaped, 3 mm ground clearance, uncoupled; sound-absorbing, rinsing, rear ventilated

Cleaning stripes: Rubber and brush, mix 2/1

Rubber profiles: serrated lengthways, for an improved wiping off effect the walking area is vaulted upwards; aluminium profile edges covered, high quality material mix, colour black; slip resistance R 9 according to DIN 51130

Brush: ARWEI three-way brush; brushes on different levels for an improved absorption of coarse dirt, quieting, colour black, slip resistance R 13 according to DIN 51130

Connection: ARWEI Special Connectors (patented in 1977); therefore easily to roll up, modular construction – no wire or cable connections -, each part can easily be replaced on the spot

Height: 23 mm

Bar distance 3 mm: coarse dirt absorption 6.6 l / sq. m; 36 brush profiles each m of walking depth

Bar distance 5 mm: coarse dirt absorption 7.5 l / sq. m; 33 brush profiles each m of walking depth

Angle frames in 25 x 25 x 3 mm are available in aluminium, brass or stainless steel.

Changes in construction or due to material reserved in the course of product maintenance. All specifications are standard dimension without consideration of tolerances contingent upon production.

# Text boxes

ARWEI Three-Way Brush

ARWEI Special Connectors

Rubber

Aluminium Profile