ARWEI-Premium-Reinstreifer

Data Sheet Portal Klassiker 17

Tender Specification:

High quality, especially wear-resistant entrance mat

Application: Indoor; suitable for heat up to 45°C; normal up to extremely strong frequency, passable by shopping trolley, pump truck, etc., suitable for wheelchairs, overall laying

Stripe supporting profile: plastic, anthracite, sound-absorbing, rinsing, rear ventilated

Needle felt special ground: 100 % PP; pole density 2,400 g / sq. m; completely needled; no sling ware, minimum contamination; extremely wear-resistant; safe by hidden screw connection; needle felt can be substituted subsequently; colours anthracite, light grey, Copenhagen blue; coconut, special colours on demand; slip resistance R 11 according to DIN 51130

Connection: ARWEI Special Connectors; therefore easily to roll up; high slip resistance due to anti-slip function; modular construction – no wire or cable connections -, each part can easily be replaced on the spot

Height: 17 mm

Bar distance 4 or 6 mm

Angle frames in 20 x 20 x 3 mm are available in aluminium, brass or stainless steel.

Changes in construction or due to material reserved in the course of product maintenance. All specifications are standard dimension without consideration of tolerances contingent upon production.

# Text boxes

Plastic Profile

Needle Felt

ARWEI Special Connectors