ARWEI-Premium-Reinstreifer

Data Sheet Portal NK 22

Tender Specification:

High quality, especially wear-resistant entrance mat

Application: Indoor and roofed exterior; normal up to extremely strong frequency, suitable for wheelchairs, overall laying, resting distributed burden up to 900 kg per 80 sq. cm

Stripe supporting profile: aluminium, V-shaped, with patented scratching edges which do not reduce the needle felt walking area; 3 mm ground clearance, uncoupled; sound-absorbing, rinsing, rear ventilated

Needle felt special ground: 100 % PP; pole density 2,400 g / sq. m; completely needled, no sling ware, minimum contamination; extremely wear-resistant; aluminium profile edges covered halfway through; safe by hidden screw connection; needle felt can be substituted subsequently; colours anthracite, light grey, Copenhagen blue, coconut, special colours on demand; slip resistance R 11 according to DIN 51130

Connection: ARWEI Special Connectors (patented in 1977); therefore easily to roll up, modular construction – no wire or cable connections -, each part can easily be replaced on the spot

Height: 22 mm

Bar distance 3 mm: coarse dirt absorption 7.5 l / sq. m; needle felt walking area 77 cm and 24 scratching edges    each m of walking depth

Bar distance 5 mm: coarse dirt absorption 8.5 l / sq. m; needle felt walking area 72 cm and 22 scratching edges    each m of walking depth

Angle frames in 25 x 25 x 3 mm are available in aluminium, brass or stainless steel.

Changes in construction or due to material reserved in the course of product maintenance. All specifications are standard dimension without consideration of tolerances contingent upon production.

# Text boxes

Aluminium Profile

Scratching Edge

Needle Felt

ARWEI Special Connectors