ARWEI-Premium-Reinstreifer

Data Sheet Portal SG 42

Tender Specification:

High quality, especially wear-resistant entrance mat, improved absorption of coarse dirt

Application: Indoor and exterior; normal up to extremely strong frequency, passable by shopping trolley, pump truck, car, etc., suitable for wheelchairs, overall laying, resting distributed burden up to 3,400 kg per 80 sq. cm

Stripe supporting profile: aluminium, V-shaped, 3 mm ground clearance, uncoupled, sound-absorbing, rinsing, rear ventilated

Rubber profiles: serrated lengthways, for an improved wiping off effect the walking area is vaulted upwards; aluminium profile edges covered, high quality material mix, colour black; slip resistance R 9 according to DIN 51130

Connection: ARWEI Special Connectors (patented in 1977); therefore easily to roll up, modular construction – no wire or cable connections -, each part can easily be replaced on the spot

Height: 42 mm

Bar distance 3 mm: Coarse dirt absorption   9.9 l / sq. m

Bar distance 5 mm: Coarse dirt absorption 12.0 l / sq. m

At a bar distance of 3 mm also appropriate for automatically revolving doors according to DIN 18650-1

Angle frames in 45 x 30 x 3 mm are available in aluminium, brass or stainless steel.

Changes in construction or due to material reserved in the course of product maintenance. All specifications are standard dimension without consideration of tolerances contingent upon production.

# Text boxes

ARWEI Special Connectors

Rubber

Aluminium Profile