ARWEI-Premium-Reinstreifer

Data Sheet Portal SN 42

Tender Specification:

High quality, especially wear-resistant entrance mat

Application: Indoor and roofed exterior; normal up to extremely strong frequency, passable by shopping trolley, pump truck, car, etc., suitable for wheelchairs, overall laying, resting distributed burden up to 3,800 kg per 80 sq. cm

Stripe supporting profile: aluminium, V-shaped; 3 mm ground clearance; uncoupled; sound-absorbing, rinsing, rear ventilated

Needle felt special ground: 100 % PP; pole density 2,400 g / sq. m; completely needled; no sling ware, minimum contamination; extremely wear-resistant; aluminium profile edges covered halfway through; safe by hidden screw connection; needle felt can be substituted subsequently; colours anthracite, light grey, Copenhagen blue; coconut, special colours on demand; slip resistance R 11 according to DIN 51130

Connection: ARWEI Special Connectors (patented in 1977); therefore easily to roll up; modular construction – no wire or cable connections -, each part can easily be replaced on the spot

Height: 42 mm

Bar distance 3 mm: coarse dirt absorption   9.9 l/ sq. m; needle felt walking area 77 cm each m of walking depth

Bar distance 5 mm: coarse dirt absorption 12.0 l/ sq. m; needle felt walking area 72 cm each m of walking depth

At a bar distance of 3 mm also appropriate for automatically revolving doors according to DIN 18650-1

Angle frames in 45 x 30 x 3 mm are available in aluminium, brass or stainless steel.

Changes in construction or due to material reserved in the course of product maintenance. All specifications are standard dimension without consideration of tolerances contingent upon production.

# Text boxes

Aluminium Profile

Needle Felt

ARWEI Special Connectors